## Slide 1: The Operational Amplifier
Op Amp and Ideal Op Amp Model
Typical Op Amp Circuits
Analysis of Op Amp circuits

## Slide 2: Op Amp and Ideal Op Amp Model
-IN
OUT
V+
V-
+IN
Op Amp :
Operational Amplifier
Practical Op Amp :
Highly integrated circuit, used to realize amplifier, mathematical operations.
  Multi-terminal devices,
  Need power supply,
  Usually have two inputs and an output

## Slide 3
LM324 Pin Connections (Top View)

## Slide 4
Circuit inside an op amp

## Slide 5: Op Amp and Ideal Op Amp Model
b
a
d
v
-
i
+
i
-
v
+
v
o
c
VS+
VS-
Op Amp Model :
a: v- : inverting input
b: v+ : noninverting input
c: vo : output
Ideal Op Amp Rules
No current flows into either input terminal.
There is no voltage difference between the two inputs.
i-= i+= 0 , vd = v+ – v- = 0
v
o
v
-
v
+
i-
i+

## Slide 6: Typical Op Amp Circuits
Inverting amplifier
The goal of analysis of Op Amp is to obtain output and input relation.
i – = 0 KCL:
v+ = v- = 0
Virtual ground

## Slide 7: Typical Op Amp Circuits
Noninverting amplifier
Node equation at v-
Virtual short-circuited

## Slide 8: Typical Op Amp Circuits
Voltage follower
As buffer, isolator
vo is independent of RL.
vo= v-=v+= vi
v
+
v
-
R
L
i
L
v
o
v
i
+
-
v
+
v
-
R
L
i
L
v
o
v
i
R1
R2
+
-

## Slide 9: Analysis of Op Amp circuits
Analysis of Op Amp :
Find output - input relation.
Find input resistance.
Method of Analysis :
  Use nodal analysis or KCL equations.
  Start from input nodes .
  The Op amp output current is unknown, avoid the calculation of this current.

## Slide 10: Analysis of Op Amp circuits
Find v0 in terms of v1 and v2.
Example
Treat v1 , v2 and v0 as known voltages. Write node equations at unknown voltage nodes.

## Slide 11: Homework
2.15, 2.34, 2.36, 2.38

## Slide 13
an amplifier of low level signals used in process control or measurement applications and commercially available in single-package units.