## Slide 1
CNENGR 228 Digital Electronics
Lecture 4 – VHDL Fundamentals 1
Dr Zhongming Zhang
Zhongming.zhang@Lancaster.ac.uk
School of Engineering
Lancaster University

## Slide 2
Course Outline
  VHDL Design Units
  Entity
  Architecture
  Library
  Structural
  Behavioral
Concurent
Signal Assignment
Sequential
Signal Assignment

## Slide 3: Objectives
  Learn the basics of VHDL language
  Understand and use the concept of object in VHDL
  Understand and use the design units of VHDL
3

## Slide 4
  Two sets of constructs:
  Simulation
  Synthesis
  The VHDL language is made up of reserved keywords
  Can not be used as a user-defined name, E.x. ENTITY, IS, PORT, ...
  In the VHDL language part of design is descried by user-defined names
  Must start with a letter, followed by any sequence of letters,
  numbers, and underscore characters
  Two underscore cannot appear in row
  Underscore cannot be the last character
  Valid names: Hello, Wire_23, test_entity_1
  Invalid names: IN, 4x1Mux, _in4, Wire_, Wire__23
VHDL Basics
4
Notes: Simulation
– Describe the behavior of the circuit in terms of input signals, the output signals, knowledge of delays
– Behavior described in terms of occurrences of events and waveforms on signals
Synthesis
– Reverse process – inference of hardware from description
– The synthesis tool will infer a hardware architecture from the VHDL model
– When writing a VHDL program, think of the hardware that synthesis tool would infer from it

## Slide 5
  The language is, for the most part, case insensitive
  ENTITY, enti ty, Entity, EnTiTy
  AND2, and 2, A nd 2
  VHDL is white space insensitive
  VHDL statements are terminated with a semicolon “ ; “
  Comment support
  Short comment - - This is a single line comments in VHDL
  Long comment /* This is a multiple
  line comments
  in VHDL */
VHDL Basics
5
Do not forget semicolon
Notes: Reserved words are in lower case by convention and shown in bold in this document.

## Slide 6
VHDL Design Units
6
In
Out
Signals
Architecture
or Body Code
In/Out
Entity
  Entity
  is used to define external view of any circuit or subcircuit (i.e. symbol)
  Defines the circuit name and ports (inputs/outputs)
  Architecture
  Used to define the functionality and timing of the model (i.e. schematic)
  Library/Package
  A LIBRARY is a directory that contains a package or a collection of packages.
  Any circuit or subcircuit in VHDL can be define using the following design units
name of circuit

## Slide 7
VHDL Design Units
Library/ Package declarations
ENTITY
ARCHITECTURE
7
Basic VHDL Code structure

## Slide 8
entity <entity_name> is
Generic declarations
Port Declarations
end entity <entity_name>; (1076-1993 version)
  Symbol name
  <entity_name> can be any alpha/numerical name
  Port declarations
  Used to describe the inputs and outputs i.e.pins
  Generic declarations
  Used to pass information into a model by defining constants
  Close entity in one of these ways
  END ENTITY <entity_name>; END <entity_name>;
Entity
8

## Slide 9
a
b
Half-adder (HA)
Entity
a
b
  Example: Half adder circuit
entity Half-adder is
port (
a, b: in BIT;
s, co: out BIT
);
end entity Half-adder;
Architecture
s = a’ . b + a . b’
co = a . b
Library
co
s
co
s

## Slide 10
  ARCHITECTURE < identifier> of <entity_name> is
  Behavioral: how designs operate
    Assignment and built-in logic operators
    Functional and/or timing
  Structural: netlist
    Gate/component level
  Hybrid:mixture of the two styles
  End architecture with
  END ARCHITECTURE <identifier>; --VHDL'93 &later
  END ARCHITECTURE; --VHDL '93 & later
Architecture
10
consists of statements describing the circuit functionality

## Slide 11
s
co
b
0
1
0
1
a
0
0
1
1
Inputs
Outputs
Architecture
Behavioral
Description 1
Description 2
Library
Entity
Structural
C1
C2
Architecture
OR
a
b
s
co
C1
C2
  Example: Half-adder circuit
Description 1
Description 2
s = a’ . b + a . b’
co = a . b
0
1
1
0
0
0
0
1

## Slide 12
architecture <identifier> of <entity_identifier> is
SIGNAL temp: INTEGER :=1;
CONSTANT load: BOOLEAN:=true;
--Component declarations (discussed later)
begin
Process statements
Concurrent procedural calls
Concurrent signal assignment
Component instantiation statements
Generate statements
end architecture <identifier>;
Architecture
12
Behavioral
Description 1
Description 2
Library
Entity
Structural
C1
C2
Architecture
OR

## Slide 13
  An object whose value may not be changed.
  Associates value to name
  Increases code flexibility
  Object: an object is a named item that has a value of a given type
Objects in VHDL
Objects in VHDL
Signal
Variable
Constant
File
  Keep history of time in simulation
  Represents wire between circuits
  Represents input/output of logic circuits
  Not having history of time in simulation
  Represent temporary output of logic circuits
13

## Slide 14
  Signal, variable, constant
Objects in VHDL
Signal
Name
Range
Value
scalar
vector
Type
std-logic
bit
integer
14

## Slide 15
  A LIBRARY is a directory that contains a package or a collection of packages
  Two types of libraries
  Library WORK
    folder where the project files are saved
  Resource libraries
    STD library
    IEEE developed packages
    Altera component packages
    Any LIBRARY of design units that is referenced in a design
Library/Package
15

## Slide 16
A Quick Homework Exercise
16
  Try to locate the STD, IEEE, and Altera libraries in the directory where
  Altera Web Edition software is installed and name some of the packages
  acossiated with each library.
Example: C:/altera/10.0/quartus/libraries

## Slide 17
  Referencing a packge requires 2 clauses
  LIBRARY clause to declare a specific library
  USE clause to declare a specific package
Library/Package
17
library library_name;
use library_name.package_name.all;
  Example
library ieee;
use ieee.std_logic_1164.all;
use WORK.filt_cmp.all;
User-defined package
Pre-defined package

## Slide 18
  LIBRARY STD
  Package STANDARD-Data types:
    Pre-defined data types (BIT, INTEGER, Boolean, ...)
    Operator functions to support pre-defined data types
    visible by default
  Package TEXTIO
    File operations
STD Library
18

## Slide 19
  Type BIT
  Two logic values '0', '1'
  Bit_vector array of bits
  signal temp: BIT_VECTOR (3 downto 0);
  signal temp: BIT_VECTOR (0 to 3);
  Each element of the bus can be accessed
Types Defined in Standard Package
19
temp:
temp(3)
temp(2)
temp(1)
temp(0)
signal <name> : <DATA TYPE> ;
signal temp: BIT;
Signal
Name
Range
Value
scalar
vector
Type
std-logic
integer
bit

## Slide 20
  Type INTEGER
  Positive and negative values in decimal -(231-1) to +(231-1)
  signal int_tmp: INTEGER; - - 32-bit number
Types Defined in Standard Package
20
variable <name> : <DATA TYPE> := <value>;
variable int_temp : integer := 16
constant <name> : <DATA TYPE> := <value>;
constant bus_width: integer := 16;
  Variables are assigned by :=
  Variable assignments are updated immediately

## Slide 21
  Type NATURAL
  Integer with range 0 to 232
  Type POSITIVE
  Integer with range 1 to 232
  Type CHARACTER
  ASCII characters
  Type STRING
  Array of characters
  Type TIME
  Value includes units of time (e.g. ps,us,ns,ms,sec,min,hr)
  Type BOOLEAN
  ‘false‘, ‘true‘
Types Defined in Standard Package
21

## Slide 22
  LIBRARY IEEE
  Package STD_LOGIC_1164-Data types:
    STD_LOGIC
    STD_LOGIC_VECTOR
    STD_ULOGIC
    STD_ULOGIC_VECTOR
  Package NUMERIC_STD-Data types:
    UNSIGNED
    SIGNED (two‘s complement)
  Package STD_LOGIC_UNSIGNED (non-standard)
  Package STD_LOGIC_SIGNED (non-standard)
IEEE Library
22

## Slide 23
  Type STD_LOGIC
  9 logic value system
  - '1': Logic value 1 or high
  - '0': Logic value 0 or low
  - 'X': Unknown
  - 'Z': (not 'z') Tri-state (high impedance)
  '-' :Don't Care
  'H': Weak logic high
  'L': Weak logic low
  'W': Weak unknown
Package STD_LOGIC_1164
23
Signal
Name
Range
Value
scalar
vector
Type
std-logic
integer
bit

## Slide 24
  Type STD_ULOGIC
  Same 9 value system as STD_LOGIC
  STD_LOGIC is called resolved type as it supports signals
  with multiple drives
  STD_ULOGIC is called unresolved type and does not support
  multiple signal drives
Package STD_LOGIC_1164
24

## Slide 25
Signal Assignment
  Signal assignment by <=
  Example
  Use double-quotes (" ") to assign multi-bit values and single-quotes (' ') to assign single-bit values
signal temp: std_logic_vector (5 downto 0) ;
signal temp: std_logic_vector (0 to 5) ;
Example:
temp <= "101010" ; -- All bits
temp (5 downto 2) <= "1010"; -- Bit slicing
temp(5) <= '1'; -- Single bit
Signal
Name
Range
Value
scalar
vector
Type
std-logic
integer
bit

## Slide 26
Signal Assignment
  Vector: <# of bits> <base> <number>
  4 b 0111
  VHDL supports ‘x’ for hexadecimal, 'o' for octal and 'b' for binary
Signed (s) /Unsigned (u)
Can contain meta-values (‘U’ - uninitialized. This signal hasn't been set yet. ‘X’ - unknown. Impossible to determine this value/result. ‘Z’ - High Impedance.)
Case insensitive
  Example:
temp <= 6x"0f";
temp <= 6Ux"f";
temp <= 6sb"11";
temp <= 6uO"7";
-- specify width 6 means "001111"
-- "001111" (zero extension)
-- "111111" (binary format)
-- "000111" (octal format)
Notes: The comments in the example are not the result of executing the assignments, but they are explaining how the applied formatting should be interpreted by the programmer.
For example, the formatting applied to the second expression shows a 6-bit unsigned hexadecimal number “f”. Therefore, it is written as '001111' in the binary format.
* The letter U here is showing unsigned number rather than uninitialized
The formatting applied to the third expression shows a 6-bit signed binary number “11”. Therefore, "11" is written as a 6-bit signed binary number by adding leading 1's to the number.
* The letter s here refers to a signed number.
Finally, last example is a 6-bit unsigned octal number. Therefore, it is written in the binary form by adding the leading zeros.
The meta values mentioned in the slide can be used instead of the (binary) numbers and they are not changing the format of the numbers. For example, it is possible to write a number as "100X" or "UU10".

## Slide 27
Practical 3 - Exercise 1
  Simple code to connect the SW switches to the LEDR lights
LEDR(17) <= SW(17);
LEDR(16) <= SW(16);
. . .
LEDR(0) <= SW(0);

## Slide 28: Summary
  Basics of VHDL language
  Design units in VHDL language: Entity, Architecture, Library
  Concept of objects in VHDL: Signal, Constant, Variable

## Slide 29
  Structure: <class> object_name: <mode> <type>;
  <class>: what can be done to an object
  Objec_name: identifier
  <mode>: directional
  - in - out - inout (bidirectional) - buffer (output with internal feedback)
  <type>: What can be contained in the object
Entity - Port Declarations
entity <entity_name> is
Generic declarations
port (
SIGNAL clk, clr : in BIT;
- - note: SIGNAL is assumed and is not required
Q: out BIT
);
end entity <entity_name>;
29

## Slide 30
  Generic values can be overwritten during compilation
  Generic must resolve to a constant during compilation
Entity - Generic Declaration
30
entity <entity_name> is
generic(
constant tplh, tphl : time:=5 ns;
- - Note constant is assumed and is not required
tphz, tplz : TIME :=3ns;
default_value : INTEGER:=1;
cnt_dir : STRING:=“up“
);
Port declarations
end entity <entity_name>;

## Slide 31
Signal
Name
Range
Value
Type
std-logic
bit
integer
scalar
vector

## Slide 32
  Example: Door Opener Circuit
Architecture
32
Behavioral
F = c' * (h + p)
Library
Signals f1, f2
Entity
Structural
C1
C2
C3
Architecture
OR
Door Opener
c
h
p
F
F = c' * (h + p)
f1
f2
C3
C2
C1

## Slide 33
  Example: Door Opener Circuit
Entity
33
Door Opener
c
h
p
F
F = c' * (h + p)
entity DoorOpener is
port (
c, h, p: in BIT;
F: out BIT
);
end entity DoorOpener;
Architecture
F = c' * (h + p)
Library
Signals f1, f2
f1
f2

## Slide 34
https://www.csee.umbc.edu/portal/help/VHDL/design.html
Really Good Resource