## Slide 1
CNENGR 228 Digital Electronics
Lecture 6 – VHDL Fundamentals 3
Dr Zhongming Zhang
School of Engineering
Lancaster University

## Slide 2
Course Outline
  VHDL Design Units
  Entity
  Architecture
  Library
  Structural
  Behavioral
Concurent
Signal Assignment
Sequential
Signal Assignment

## Slide 3: Objectives
  After completion of this lecture you will
  Behavioral vs Structural description of architecutre
  VHDL Statements-Sequential signal assignment
  Testbench simulation
3

## Slide 4: Structural Description
Top-level module: the module that has not been used in other circuits
Design hierarchy: a design can use multiple sub-modules or a module multiple times
Inputs
Top-level module
M1
M3
M2
M1
M2
M1
M1
Outputs
low-level
modules
4

## Slide 5
Example
  Component Declaration
  Component Instantiation
    Using a module in another top-level.
    Label to identify unique instance of component.
    Component type to select the desired declared component.
    Port map to connect ports of components of sub-modules to that of top-level design.
c
h
p
f
Using Sub-circuits
Top-level module
n1
n2
OR2
x
y
F
Inv
x
F
AND2
F
x
y
c
h
p
f
Top-level module
n1
n2
OR2_1
AND2_1
Inv_1

## Slide 6
  To declare the Port types and the Data Types of the ports for a lower-level design a component construct is used.
component <lower-level_design_name>
port (
<port name>: <mode> <data type> ;
<port name>: <mode> <data type>
);
end component
Component Declaration
6
c
h
p
f
Inv
x
F
n1
n2
Inv_1
component Inv
port ( x : in std_logic;
F : out std_logic);
end component;
Top-level module

## Slide 7
Component Instantiation
7
Inv_1: Inv port map (x => c, F => n1);
label
component type
Output of NOT gate on Inv
(low-level port)
n1: internal signal
in the parent architecture
Inv
x
F
c
h
p
f
n1
n2
Inv_1
<instance>: <component>
port map (
<port> => <parent signal or port>,
<port> => <parent signal or port>);

## Slide 8
component declaration
component instantiation
architecture circuit of DoorOpener is
begin
end architecture circuit;
8
Door Opener
c
h
p
f
AND2_1
OR2_1
Inv_1
n2
n1
Design Hierarchy
entity DoorOpener is
port ( c, h, p: in std_logic;
f: out std_logic);
end entity DoorOpener;
Library ieee;
use ieee.std_logic_1164.all;
signal n1, n2 : std_logic;

## Slide 9
9
Design Hierarchy
Inv_1: Inv port map (x => c, F => n1);
OR2_1: OR2 port map (x => h, y => p, F => n2);
AND2_1: AND2 port map (x => n1, y => n2, F => f);
component Inv
port ( x : in std_logic;
F : out std_logic);
end component;
component OR2
port ( x, y : in std_logic;
F : out std_logic);
end component;
component AND2
port ( x, y : in std_logic;
F : out std_logic);
end component;
Component Instantiation
Component declaration
Door Opener
c
h
p
f
AND2_1
OR2_1
Inv_1
n2
n1

## Slide 10
  This component-based approach uses component declarations and component instantiations
Design Hierarchy
DoorOpener.vhd
Entity-Architecture “top-level”
Component “Inv”
Component “OR2”
Component “AND2”
Inv.vhd
entity-architecture “Inv”
OR2.vhd
entity-architecture “OR2”
10
AND2.vhd
entity-architecture “AND2”

## Slide 11
Practical 3-Exercise 2 (behavioral description)
Practical 5a-Exercise 1 (structural description)
  Implement a 2-to-1 multiplexer with a select input
x
s
m
n1
n2
n3
s
y
  (Structural description)
11
y
s
x
m
m <= (NOT (s) AND x) OR (s AND y);
  (Behavioral Description)

## Slide 12
Sequential Statements
12
process (sensitivity_list)
Constant declarations
Variable declarations
begin
- sequential assignments;
- if-else statements;
- case statements
- loop, while, for statements
end process;
Sequential statements
  A “process” block contains one or more sequential statements and sequential assignments
Local objects
  Here, sequential statements are used inside a process
  They are evaluated in the order in which they appear in the code (sequential) and describe the behaviour

## Slide 13
Sequential Statements
Library
Entity
Architecture
process (a, b, c)
begin
c <= a and b;
y <= c;
end process;
  A sensitivity list identifies signals whose events resume the process.
  For combinational logic, include every signal read, including conditions.
  VHDL-2008: process(all) includes all signals read. A plain process does not.
  Process is sensitive to sensitivity list
Library
Entity
Architecture
process(all)
begin
c <= a and b;
y <= c;
end process;

## Slide 14
  Timed waits model testbench delays. Supported clock-edge waits can describe synthesizable registers.
  Three types
  wait for <time_ expression>: pauses until time specified by the expression has elapsed.
  wait on <signal>: pauses until signal event occurs.
  wait until: resumes on a signal event when the condition is true.
Wait Statements
    wait for 20 ns;
    wait on a;
    wait until (int < 100);
    wait on a for 5 us;

## Slide 15
Process block: Quick Notes
  Sensitivity list implies a wait statement at the end of the process
  A process repeats; a wait or sensitivity list suspends it until it can resume.
  Process can not have both a sensitivity list and wait statement.
  Concurrent signal assignments represent implied processes operating in parallel
proc1 : process (a,b)
begin
Sequential statements;
end process;
proc2 : process
begin
Sequential statements;
wait on a, b;
end process;

## Slide 16
Sequential Statements
Sequential Statements
Case
statements
Loop
statements
Sequential assignments
Simple signal assignment
Variable
assignment
process (sensitivity_list)
begin
- sequential assignments;
- if-else statements;
- case statements
- loop, while, for statements
end process;
Sequential statements
If-then
statements

## Slide 17
Sequential assignment
Sequential Statements
Case
statements
If-then
statements
Loop
statements
Sequential assignments
Simple signal assignment
Variable
assignment
  Variable assignment denoted by :=
    Executes sequentially; the variable updates immediately.
  Signal assignment denoted by <=
    Executes sequentially and schedules an update. With no explicit delay, the signal updates in a later delta cycle after suspension.

## Slide 18
Sequential assignment
One activation: trigger changes from 0 to 1; initial s_var = s_sig = 2.
signal trigger : bit := '0'; -- before architecture begin
Variable assignment
Signal assignment
process(trigger)
variable s_var : integer := 2;
variable a_var : integer := 0;
begin
if trigger = '1' then
s_var := 4;
a_var := s_var;
end if;
end process;
-- before architecture begin:
signal s_sig : integer := 2;
signal a_sig : integer := 0;
-- after architecture begin:
process(trigger)
begin
if trigger = '1' then
s_sig <= 4;
a_sig <= s_sig;
end if;
end process;
s_var = 4, a_var = 4
s_sig = 4, a_sig = 2
Variables update immediately.
The second statement reads the new value.
Results shown after scheduled updates.
The second statement reads the current value.

## Slide 19
process (a , c)
begin
d <= a and c;
end process
Overall Code Parallelism
  Statements inside a process block are evaluated sequentially.
  However, all process blocks are evaluated concurrently.
  All concurrent signal assignments are evaluated concurrently too.
  Example: a <= ‘0’; b <= ‘0’;
process (c, d)
begin
e <= (not(d) and c) or (d and not(c));
end process
c <= a xor b;
a
b
d
c
e

## Slide 20
Practical 5b- VHDL Testbench
  Assigns values to a system's inputs, check that system outputs correct values
  A key use of HDLs is to simulate system to ensure design is correct
23
System To Test
Testbench
Set input values, Check output values

## Slide 21
  Entity of Testbench
  No inputs or outputs
  Architecture of Testbench
  Declares component to test, declares signals.
  Instantiates component, connects to signals.
  Process writes input signals, checks output signal.
Circuit
Under Test
System
To Test
Set input values, Check output values
Process
Entity-Testbench
Architecture
24
Practical 5b- VHDL Testbench

## Slide 22: Summary
  Familiarity with structural description of architecture
  Introducing the concept of process in VHDL
  Introducing the Testbench for simulation of circuits

## Slide 23: Hints for Practical 5a-Exercise 1
y
s
x
m
x
y
s
m

## Slide 24: Hints for Practical 5a-Exercise 1
Netlist Viewers -> RTL Viewer
Netlist Viewers -> Technology Map Viewer (Post-Mapping)

## Slide 25: Hints for Practical 5a-Exercise 2

## Slide 26: Hints for Practical 5a-Exercise 2

## Slide 27: Hints for Practical 5a-Exercise 2

## Slide 28: Hints for Practical 5a-Exercise 2 (defined using “simple signal assignment”)

## Slide 29: Hints for Practical 5a-Exercise 2

## Slide 30
24
EqTest1.vhd
EqTest2.vhd
EqTest3.vhd
Practical 5b- VHDL Testbench
a
b
y
a
b
y
a
b
y